LP-15 (R)

A. FOR THE SERIAL INTERFACES

THE PROTOCOLS FOR THE CAS STANDARD SERIAL INTERFACE

THIS IS HALF-DUPLEX COMMUNICATION RS-232C.

A. 1 THE COMMUNICATION AGREEMENTS 1. BAUD RATE -> 9,600 BPS

2. DATA BIT -> 8 BIT

3. STOP BIT -> 1 BIT

4. PATIRITY BIT -> NO

-> RS-232C LEVEL

5. COMMUNICATION LEVEL

6. DATA FORMAT -> ASCII

7. THE COMMAND DEFINITIONS

A. 2 THE WIRE CONNECTIONS

A. 2. 1 THE WIRE CONNECTIONS OF THE D-SUB 9 PIN CONNECTOR OF A COMPUTER SIDE

COMPUTER RXD(PIN 2) TXD(PIN 3) GND(PIN 5) RTS(PIN 7) CTS(PIN 8) DTR(PIN 4) DSR(PIN  6)

SCALE

TXD(PIN  2)

RXD(PIN 3) GND(PIN 7)

A. 2. 2 THE WIRE CONNECTIONS OF THE D-SUB 25 PIN CONNECTOR OF A COMPUTER SIDE

SCALE TXD(PIN 2) RXD(PIN 3) GND(PIN 7)

COMPUTER RXD(PIN 3) TXD(PIN 2) GND(PIN 7) RTS(PIN 4) CTS(PIN 5) DCD(PIN 8) DSR(PIN 6) DTR(PIN 20)